PC power consumption

Bernd Panzer-Steindel, CERN/IT/ADC

30.07.2002

- Power supply efficiency is about 70 % ==    70 W effective power needs 100 W input power

- Mainboard + power supply + harddisk under load consume on a dual cpu board

(PIII 1 GHz) up to 100 W more (variation of up to 30 % depended on the motherboard

and power supply)

- The latest dual cpu Itanium 2 box from HP requires  about 700 Watts of input power

- Ratio of SpecInt95 versus SpecInt2000 is about 0.1       1 SpecInt95 = 10 SpecInt2000

- Disk power consumption is about 10 W at idle time and 30 W at startup  (120 GB EIDE disk)

- Estimated needs for LHC computing in 2007 is    2.3 million  SpecInt95 and 3100 TB

(   at a ratio of  10 SpecInt2000 / Watt   ==  2.3 MW power for the CPU server

(   with 1 TB disks at 30 W                     ==  0.1 MW

but scaling not yet really checked       current   GB/W curve

- PIII   Northwood (0.18 um)  256 KB L2                          == 28 million transistors

PIII   Willamette (0.13 um)  256 KB L2                          == 28 million transistors

PIV   (0.18 um)  256 KB L2                                             ==  42 million transistors

PIV   (0.13 um)  512 KB L2                                             ==  55 million transistors

Itanium 2  Mcinley (0.18 um) 256 KB L2 + 3 MB L3     ==  220 million transistors

Itanium 2  Maddison (0.13 um) 256 KB L2 + 6 MB L3   ==  500 million transistors

(L3 on chip !) ( power